## Slide 1
Enhanced environmental protection inspection for efficient control of air quality monitoring and of all entities under obligation within system of greenhouse gas emission allowance trading, in order to achieve better quality of air in Republic of Croatia
This project is funded by the European Union

## Slide 2: THEME 2: Pollutants

## Slide 3: 2.1 SO2 – CHEMICAL CHARACTERISTICS
Sulphur dioxide (SO2) is a colourless gas that most people can smell it in the range of concentration of 1000 to 3000 μg/m3 of air. At higher concentrations (above 10 000 μg/m3 air) the smell of him is irritating.
European Union IPA 2013 Programme for Croatia

## Slide 4: 2.2 SO2 – CHEMISTRY OF PRODUCTION AND DEGRADATION
Released into the atmosphere, sulphur (S) reacts with oxygen (O2) and produced sulphur dioxide (SO2):
S + O2  SO2
Sulfur dioxide (SO2) in the atmosphere can also occur by oxidation of hydrogen sulphide (H2S):
2H2S + 3O2  2SO2
SO2 can be dissolved in the water and in the form of water vapor or rain in the atmosphere forming sulphurous acid (H2SO3):
SO2 + H2O  H2SO3
European Union IPA 2013 Programme for Croatia

## Slide 5: 2.2 SO2 – CHEMISTRY OF PRODUCTION AND DEGRADATION
SO2 can also be oxidized or reacted in the atmosphere in catalytic or photochemical reactions with other air pollutants. Sulfur trioxide, sulfuric acid and sulfates are produced from such reactions:
2SO2 + O2  2SO3
Sulphur trioksid (SO3) is a very reactive gas and in the presence of water vapor in the air very quickly hydrates in sulfuric acid (H2SO4).
SO3 + H2O  H2SO4
European Union IPA 2013 Programme for Croatia

## Slide 6: 2.2 SO2 – CHEMISTRY OF PRODUCTION AND DEGRADATION
Sulfuric acid can react with other components of air, products sulfate.
Some sulphates are emitted into the air from industrial plants, but also from natural sources such as volcanic eruptions.
European Union IPA 2013 Programme for Croatia

## Slide 7: 2.2 SO2 – CHEMISTRY OF PRODUCTION AND DEGRADATION
Natural sources
Sulphur compounds in the unpolluted air is located in very small concentrations. In the air can be found in:
Gaseous phase (H2S) i (SO2)
Shape of the particles as sulphates.
Sulphur dioxide and hydrogen sulphide into the atmosphere are emitted during the volcanic eruptions or from the soil in which occur as a result of the metabolism of anaerobic bacteria.
In the form of sulphate particles can also be emitted directly out of a volcano, or carried by the wind from the ocean surface.
European Union IPA 2013 Programme for Croatia

## Slide 8: 2.2 SO2 – CHEMISTRY OF PRODUCTION AND DEGRADATION
Natural sources (example)
After the eruption of the volcano Mt. Pinatubo in the Philippines, 1991. the cloud which contained SO2 in the next 10 days spread over half of the equatorial part reaching to the west coast of Africa. Source: NASA.
European Union IPA 2013 Programme for Croatia

## Slide 9: 2.2 SO2 – CHEMISTRY OF PRODUCTION AND DEGRADATION
Anthropogenic sources
Anthropogenic sources of sulfur compounds are the most common from combustion of fossil fuels in factories for the production of energy for heating and motor vehicles.
coal burning
oil and gasoline burning
oil refineries
European Union IPA 2013 Programme for Croatia

## Slide 10: 2.2 SO2 – CHEMISTRY OF PRODUCTION AND DEGRADATION
Natural and anthropogenic sources
Sources and locations of plunging sulfur compounds in the biosphere.
European Union IPA 2013 Programme for Croatia

## Slide 11: 2.3 SO2 – SPATIAL AND TEMPORAL DISTRIBUTION
The average annual value of the concentration of SO2 are categorized according to the location:
The improvement of air quality (refers to the concentration. SO2) in Europe in the last few decades is the result of the implementation of the national and international regulations.
European Union IPA 2013 Programme for Croatia

## Slide 12: 2.3 SO2 – SPATIAL AND TEMPORAL DISTRIBUTION
With regard to the source of pollution, the largest proportion of SO2 in the air comes from the industry, and then from the traffic.
On a global level, the concentration of SO2 in air significantly differ depending on the industrial development of countries. Most are in developing countries, slightly less in the transition countries, and lowest in the highly industrialized countries.
background
industry
traffic
developing countries
countries in transition
highly industrialized countries
European Union IPA 2013 Programme for Croatia

## Slide 13: 2.3 SO2 – SPATIAL AND TEMPORAL DISTRIBUTION
Average annual concentrations of SO2 in the world in the period of 2002. to 2005. Source: Air quality guidelines – the WHO.
European Union IPA 2013 Programme for Croatia

## Slide 14: 2.4 SO2 – TOXICOLOGICAL AND PUBLIC HEALTH ASPECTS
Pathways of SO2 entry into the body are: RESPIRATORY SYSTEM,
DIGESTIVE SYSTEM,
SKIN
SO2 is soluble in water and is absorbed through the mucous membranes of the nose and upper respiratory tract.
Example:
The amount of absorption depends on the inhaled concentration of the SO2.
If you inhale the SO2 in concentration from 4 to 6 μg/m3 of air, it will be absorbe 85% inhaled SO2
At concentrations of 46 μg/m3 of air is absorbed 99% SO2
With increased physical activity at accelerated breathing absorption is moved deeper towards the lower respiratory tract.
European Union IPA 2013 Programme for Croatia

## Slide 15: 2.4 SO2 – TOXICOLOGICAL AND PUBLIC HEALTH ASPECTS
Absorption of SO2 are created sulphite (SO32-) and bisulphite (HSO3-) ions in the following reactions:
SO2 + H2O  H2SO3
H2SO3 + H2O  HSO3- + H3O+
HSO3 - + H2O  SO32- + H3O+
Sulfite and bisulphite ions bind to nerve receptors in the upper and middle airways. They are irritant and come into contact with the airway (bronchoconstriction). Bronchoconstriction is the result of muscle contraction which carries the mucous membrane.
European Union IPA 2013 Programme for Croatia

## Slide 16: 2.4 SO2 – TOXICOLOGICAL AND PUBLIC HEALTH ASPECTS
The ambient SO2 concentrations do not constitute a danger to human health, except in places where concentrations are elevated in industrial plants smelter.
An experiment:
The highest measured one-hour average concentration in Europe in the period of 1990. to 1999. was 587 μg/m3, and the highest 24-hour average he had a value of 327 μg/m3.
It has been done on volunteers - the first symptoms occur when inhaling SO2 concentrations exceeding 14,000 μg / m3, which are much more than ambient.
European Union IPA 2013 Programme for Croatia

## Slide 17: 2.4 SO2 – TOXICOLOGICAL AND PUBLIC HEALTH ASPECTS
Recommended values (μg/m3), the concentration of sulfur dioxide (SO2) in the air-the WHO
Pollutant
Averaging time
Temporary goal 1
Temporary goal 2
Temporary goal 3
Recommended value
SO2
10 min.
24 hours
European Union IPA 2013 Programme for Croatia

## Slide 18: 2.5 – SO2 MEASUREMENT METHODS
The reference method for the measurement of SO2
Ultraviolet (UV) fluorescence
(HRN EN 14212)
Prescribed by regulations of the Republic of Croatia and the European Union. In the European Union and in Croatia, was adopted by 2012.
European Union IPA 2013 Programme for Croatia

## Slide 19: 2.5 – SO2 MEASUREMENT METHODS
SO2 + hv  SO2*
SO2*  SO2 + hv
where SO2 * is excited state of the molecule
The intensity of the emitted radiation is proportional to the number of molecules in a given volume of SO2, or the concentration of the SO2 molecule in the air.
The method is based on fluorescence of the SO2 molecule if the molecule is exposed to ultraviolet (UV) radiation. Because of exposure to UV radiation the SO2 molecule switches from normal to excited state and is then returned to normal state by emitted fluorescent radiation.
European Union IPA 2013 Programme for Croatia

## Slide 20: 2.1 CO – CHEMICAL CHARACTERISTICS
Carbon monoxide (CO) gas has no odor, color, and flavor, lighter than air and very poorly soluble in water. At standard conditions of temperature and pressure (25°C, 1 atm) is chemically inert, and becomes at a higher temperature a powerful reducing agent. A life time of a molecule of CO in the atmosphere is 0.2 years.
European Union IPA 2013 Programme for Croatia

## Slide 21: 2.2 CO – CHEMISTRY OF PRODUCTION AND DEGRADATION
CO is created incomplete combustion of organic substances (substances that contain carbon). Since the gasoline is also organic matter which consists of a mixture of different hydrocarbons, including octane (C8H18), incomplete combustion of gasoline creates a CO who is found in car exhaust fumes.
Example:
2C8H18 + 25O2  16CO2 + 18H2O
If the supply of a car engine with oxygen is sufficient, octane from the gasoline will be fully oxidized and carbon dioxide and water will produce:
European Union IPA 2013 Programme for Croatia

## Slide 22: 2.2 CO – CHEMISTRY OF PRODUCTION AND DEGRADATION
In reality, it is not converted all the carbon in carbon dioxide, is already being created and a certain amount of (about 7%) carbon monoxide. In the extreme situation all the carbon from octane will be converted to carbon monoxide:
2C8H18 + 17O2 16CO + 18H2O
CO is created on the surface of the Earth diffuses in the upper parts of the troposphere, where with the help of hydroxyl radicals is oxidized into carbon dioxide (CO2). A certain amount of CO in the atmosphere creates by oxidation biological created methane (CH4), which is a product of the decomposition of plant and animal residues, but also by a series of chemical reactions with other compounds in the atmosphere.
European Union IPA 2013 Programme for Croatia

## Slide 23: 2.2 CO – CHEMISTRY OF PRODUCTION AND DEGRADATION
The oceans represent places where CO or releases or plunges into them depending on the conditions prevailing, the partial pressure of CO in the atmosphere, the temperature of the ocean water.
Additional amounts of CO released in the atmosphere from factories, from traffic and forest fires. Microorganisms in the soil can remove a certain amount of CO in the atmosphere because it is spending for its metabolic processes.
European Union IPA 2013 Programme for Croatia

## Slide 24: 2.2 CO – CHEMISTRY OF PRODUCTION AND DEGRADATION
Global cycle CO. source: Jain, K.K. 1990. Carbon monoxide poisoning.
European Union IPA 2013 Programme for Croatia

## Slide 25: 2.2 CO – CHEMISTRY OF PRODUCTION AND DEGRADATION
Natural and anthropogenic sources
It is estimated that the annual global emissions of CO in the atmosphere are 2600 million tons
BIOLOGICAL plants and oceans
CHEMICAL oxidation of hydrocarbons in the atmosphere
Incomplete combustion of organic substances (transport, industry and households)
ANTROPOGENIC SOURCES
NATURAL SOURCES
European Union IPA 2013 Programme for Croatia

## Slide 26: 2.3 CO – SPATIAL AND TEMPORAL DISTRIBUTION
Global background concentrations of CO range from 0.06 and 0.14 mg/m3.
CO concentrations vary with respect to the location of the measurement. So the average annual values of the measured concentration of CO in the area of Europe at the locations of the stations AirBasea range from 0.4 mg/m3 in rural up to 0.7 mg/m3 in urban areas.
The ambient concentration measured in urban areas depend significantly on the density of traffic, topography and weather conditions.
European Union IPA 2013 Programme for Croatia

## Slide 27: 2.3 CO – SPATIAL AND TEMPORAL DISTRIBUTION
With regard to the source of pollution, the largest proportion of CO in the air comes from the traffic, and then from the industry.
They're much higher concentrations of CO from ambient measured in underground garages, tunnels, and other enclosed spaces with inadequate ventilation, as well as in homes, especially kitchens, where it is used city gas (peak concentration was even 60 mg/m3 ).
In connection with the traffic , the concentration of CO in the air show a clear diurnal variation with the expressed values of the peak in the morning and in the afternoon, which corresponds to the time when people go to work and return from work.
European Union IPA 2013 Programme for Croatia
Background
Industrial
Traffic

## Slide 28: 2.3 CO – SPATIAL AND TEMPORAL DISTRIBUTION
According to the data of EPA, 95% of anthropogenic emissions in the U.S. comes from road traffic, while on the second place there are emissions from the non-road traffic. The rest of the show relate to industrial sources and sources from households.
Non-road traffic
Road traffic
Industry
Combusting
European Union IPA 2013 Programme for Croatia

## Slide 29: 2.4 CO – TOXICOLOGICAL PUBLIC HEALTH ASPECTS
Since the CO gas stable in the atmosphere, the lungs are the only way of entering the organism. When CO pass alveolar and capillary membrane and enters the bloodstream, would diffuse into the blood cells and binds reversible to a protein on a hem that is an integral part of hemoglobin in erythrocytes on the place where the otherwise binds the oxygen, producing carboxyhemoglobin (COHb).
Since there is an affinity for carbon monoxide to hem 200 to 250 times higher than the affinity of oxygen, in individuals exposed to elevated concentrations of CO, poisoning occurs in very short exposure.
European Union IPA 2013 Programme for Croatia

## Slide 30: 2.4 CO – TOXICOLOGICAL PUBLIC HEALTH ASPECTS
Institut za energetiku i zaštitu okoliša
Poisoning is the result of a lack of oxygen in the tissues (hypoxia). Levels of carboxyhemoglobin is created it can be measured, and he represents a biomarker for determining exposure CO. CO from the body eliminates through the lungs.
Depending on the concentrations of carboxyhemoglobin, poisoning symptoms are different and become more serious with the increase in the concentration of carboxyhemoglobin in the blood. The organs that are the most affected ones are the organs that need oxygen the most for their function: cerebrum, the organs of the cardiovascular system and skeletal muscles.
No breathing and heart work, death
Coma, slow breathing, possible death
Tachycardia and coma
Tachycardia and coma
Headache, dizziness, vomitting
Headache
Possible headache
No symptoms
European Union IPA 2013 Programme for Croatia

## Slide 31: 2.4 CO – TOXICOLOGICAL PUBLIC HEALTH ASPECTS
Non-smokers with the occupations in which they are increasingly exposed to elevated concentrations of CO (professional drivers, traffic police officers, workers in the tunnels and garages, fire brigade, etc.) have a COHb levels permanently greater than 5%, while a larger number of smokers of cigarettes have COHb levels even higher of 13%. By measuring COHb in smokers has found that the percentage of COHb values grow to a value that is larger than 13% if the smoker within 7 hours, smoke a 29 cigarettes. If after this time if they do not smoke another cigarette, elimination of CO related to hemoglobin will be even 15 hours.
Changes in the percentage of COHb values associated with cigarette smoking and the time of elimination of CO from the organism. Source: Landaw 1973.
European Union IPA 2013 Programme for Croatia

## Slide 32: 2.4 CO – TOXICOLOGICAL PUBLIC HEALTH ASPECTS
Neurological effects
Acute poisoning of carbon monoxide may cause reversible short-term neurological deficit, but also serious neurological damage. At levels above 10% COHb headaches are possible, while at the level of about 40% COHb can occur dizziness and fainting. Psychomotor effects, such as reduced coordination and orientation, may occur at levels of COHb from 5.1 to 8.2%.
European Union IPA 2013 Programme for Croatia

## Slide 33: 2.4 CO – TOXICOLOGICAL PUBLIC HEALTH ASPECTS
Cardiovascular effects
Patients with cardiovascular disease, especially those with ischaemic heart disease, they are more susceptible to carbon monoxide than healthy people. Narrowing of the coronary arteries due to atherosclerotic change and weakened by the expansion mechanisms reduce the blood supply to the myocardium disabling the physiological compensation for reduced oxygen flow caused by elevated levels of COHb. At the level of 5% COHb in such patients affects cardiac arrhythmias that are more often after physical activity.
European Union IPA 2013 Programme for Croatia

## Slide 34: 2.4 CO – TOXICOLOGICAL PUBLIC HEALTH ASPECTS
Carcinogens and mutagenic effects
There is no evidence for carcinogenic and mutagenic effects of carbon monoxide that has been entered in the system.
European Union IPA 2013 Programme for Croatia

## Slide 35: 2.4 CO – TOXICOLOGICAL PUBLIC HEALTH ASPECTS
Recommended values (mg/m3), the concentration of carbon monoxide (CO) in the air-the. WHO
CO
min.
min.
hour
hours
Pollutant
Averaging time
Temporary goal 1
Temporary goal 2
Temporary goal 3
Recommended value
European Union IPA 2013 Programme for Croatia

## Slide 36: 2.5 CO – MEASUREMENT METHODS
The reference method for the measurement of carbon monoxide
Prescribed by regulations of the Republic of Croatia and the European Union. In the European Union and Croatia, was adopted by 2012.
Infrared (IR) spectroscopy (HRN EN 14626)
European Union IPA 2013 Programme for Croatia

## Slide 37: 2.5 CO – MEASUREMENT METHODS
The fundamental principle of the method is the possibility of CO molecules to absorb IR-radiation, and as spectroscopic analysis based on the application of the Beer-Lambert law, which describes relationship between the intensity of electromagnetic radiation before and after passing through the sample. The degree of absorption of IR-radiation depends on:
length of the absorption chamber (CO has the highest absorption on the wave length of 4.67 μm)
the absorption coefficient
the concentration of CO in the sample entered in the absorption chamber
European Union IPA 2013 Programme for Croatia

## Slide 38: 2.5 CO – MEASUREMENT METHODS
Since almost every heteroatomic molecule (especially the H2O, CO2, nitrogen oxides and hydrocarbons) absorb IR radiation, to remove interference in the carbon monoxide analysers apply and combine different methods such as:
• measuring of IR-absorption on the length of exactly 4.67 μm
• measuring with the help of two measuring chambers of which one is the reference
• measuring at multiple wavelengths, by applying the gas filter, called a correlation wheel
• drying air before entering into the measuring chamber
European Union IPA 2013 Programme for Croatia

## Slide 39: 2.5 CO – MEASUREMENT METHODS
If the instrument is calibrated in volume/volume units, the concentration of CO are measured directly in volume/volume units (ppm) because the absorption in the IR spectrum is proportional to the concentration of CO in the volume/volume units.
After that, the obtained concentrations in ppb are converted to mg/m3, using the standard conversation factors for a temperature of 20 ° C and an atmospheric pressure of 1013 hPa.
1 ppm (μmol/mol) CO = 1,16 mg/m3
European Union IPA 2013 Programme for Croatia

## Slide 40: 2.1 NO2 – CHEMICAL CHARACTERISTICS
Nitrogen dioxide is a reddish-brown gas with a characteristic irritating odor. It is soluble in water, strong oxidant, and has corrosive properties. It plays a role in the global climate change on Earth, and together with nitrogen oxide (NO) is the main regulator of the oxidizing capacity of the troposphere by controlling the destiny of the radicals, including hydroxyl radicals. Due to photolysis in the troposphere, it plays an important role in the photochemical creation of ground-level ozone (O3).
European Union IPA 2013 Programme for Croatia

## Slide 41: 2.2 NO2 – CHEMISTRY OF PRODUCTION AND DEGRADATION
The nitrogen oxides (NOx) in the troposphere, transformed and removed from it through a complex chemical reaction involving and photochemical reactions that create ground level ozone and photochemical smog.
The dominant source of nitrogen oxide in the air are the processes of burning.
90 to 95% of the nitrogen oxides emitted as nitric oxide (NO), and 5 to 10% as nitrogen dioxide (NO2).
European Union IPA 2013 Programme for Croatia

## Slide 42: 2.2 NO2 – CHEMISTRY OF PRODUCTION AND DEGRADATION
Creation of photochemical smog
2NO + O2  2NO2
NO2 + Sunlight O + NO
In the creation of photochemical smog NO from motor vehicles, a starting compound is oxidized to the troposphere by forming nitrogen dioxide (NO2)
The created NO2 is photolyzed in a photolytic reaction producing nitrogen oxide and oxygen:
European Union IPA 2013 Programme for Croatia

## Slide 43: 2.2 NO2 – CHEMISTRY OF PRODUCTION AND DEGRADATION
The oxygen atom (O), which is created in the preceding reaction in a very fast reaction reacts with a molecule of oxygen (O2) creating a molecule of ozone (O3). In this reaction, the participating and molecules that are marked with the «M», and represent the N2, O2, etc., that have a role in the absorption of vibration energy from the newly synthesized molecule of ozone (O3):
O + O2 + M  O3
Molecule of nitric oxide (NO), which is created in the reaction [2] reacts with ozone (O3) from reaction [3].
NO + O3  NO2 + O2
European Union IPA 2013 Programme for Croatia

## Slide 44: 2.2 NO2 – CHEMISTRY OF PRODUCTION AND DEGRADATION
In this series of chemical reactions do not create new products or break down the existing and therefore this cycle got the name of the zero cycle.
After this series of chemical reactions, the question is: how there is an increase in the concentration of NO2 and O3 during the day in the troposphere? Something is missing!
For creation of photochemical smog, you need the organic compounds in the air, such as:
VOC – volatile organic compound
ROC – reactive organic carbon
NmHC – nonmethane hydrocarbons.
European Union IPA 2013 Programme for Croatia

## Slide 45: 2.2 NO2 – CHEMISTRY OF PRODUCTION AND DEGRADATION
Urban troposphere is abundant with these compounds, and with favorable conditions result in the creation of photochemical smog.
The first condition is the creation of hydroxyl radicals (OH), which is formed by the reaction of free radicals O * and water molecule (O * excitedis form of atomic oxygen):
O3 + Sunlight  O2 + O*
O* + H2O  2OH
European Union IPA 2013 Programme for Croatia

## Slide 46: 2.2 NO2 – CHEMISTRY OF PRODUCTION AND DEGRADATION
The hydroxyl radical is the most important oxidizing agent in the troposphere and it can react with all the organic compounds in the air. The products of these reactions are water molecules (H2O) and organic radicals:
RH + OH  H2O + R*
where is the R (CH3 or CHO or CH2CH3) and R * is an organic radical
R* + O2 + M  RO2* + M (very quick response)
RO2 * allows NO oxidation in NO2 without degradation of ozone molecule (O3)
RO2* + NO  NO2 + RO*
European Union IPA 2013 Programme for Croatia

## Slide 47: 2.2 NO2 – CHEMISTRY OF PRODUCTION AND DEGRADATION
Summary cycle of organic radicals creation
European Union IPA 2013 Programme for Croatia

## Slide 48: 2.2 NO2 – CHEMISTRY OF PRODUCTION AND DEGRADATION
In photochemical reactions in the troposphere by oxidation of NOX, products such as HNO3, HO2NO2, HNO2, peroxiacetyl nitrates, N2O5, nitrate radicals and organic nitrates are produced and all together represent biological irritants.
European Union IPA 2013 Programme for Croatia

## Slide 49: 2.2 NO2 – CHEMISTRY OF PRODUCTION AND DEGRADATION
Summary the creation of photochemical smog
Photochemical smog is a mixture of primary and secondary pollutants in the troposphere.
Photochemical smog is created by a series reactions in which it transforms nitrogen (N) in the different compounds in the atmosphere.
3. Cars emit NO and small amounts of NO2
European Union IPA 2013 Programme for Croatia

## Slide 50: 2.2 NO2 – CHEMISTRY OF PRODUCTION AND DEGRADATION
Nitric oxide (NO) is actually the starting compound that is oxidized to atmospheric nitrogen dioxide (NO2), and he is further oxidized to nitric trioksid (NO3), which is transformed into nitric pentoksid (N2O5). Each of these nitrogen oxides then reacts in the photochemical processes with other atmospheric compounds, creating numerous biological irritants.
In the reactions of the creation of photochemical smog comes also to the deposition of ground-level ozone (O3) in the lower layers of the troposphere
The resulting mixture of photochemical smog consists of more than 100 chemical compounds.
European Union IPA 2013 Programme for Croatia

## Slide 51: 2.2 NO2 – CHEMISTRY OF PRODUCTION AND DEGRADATION
Natural and anthropogenic sources
INDUSTRY
TRAFFIC
FOREST FIRES, biological processes in soil
European Union IPA 2013 Programme for Croatia

## Slide 52: 2.3 NO2 – SPATIAL AND TEMPORAL DISTRIBUTION
The types and concentrations of nitrogen compounds can vary a lot depending on:
Location
part of the day,
time of year
The main anthropogenic source of nitrogen oxides is combustion processes. Fossil fuels that burn in thermoelectric power plants, car engines and small household heating boilers emit nitrogen oxides most often in the form of nitrogen oxides (NO) and only 10% in the form of nitrogen oxides (NO2).
European Union IPA 2013 Programme for Croatia

## Slide 53: 2.3 NO2 – SPATIAL AND TEMPORAL DISTRIBUTION
Natural sources include volcanoes, forest fires, and biological processes in the soil which are released mainly nitrous oxide (N2O). Processes in which it comes to the formation of NO2, besides the combustion of fossil fuels, are nitrification and denitrification with the help of bacteria in the soil, as well as an electrical discharge in the atmosphere (the lightning).
The main mechanism of removal of nitrogen oxide in the atmosphere is HNO3 oxidation followed by dry or wet deposition and the absorption of nitric acid in the soil.
European Union IPA 2013 Programme for Croatia

## Slide 54: 2.3 NO2 – SPATIAL AND TEMPORAL DISTRIBUTION
Except that pollute the atmosphere, nitrogen compounds entered into the soil by artificial fertilizers in agriculture, pollute the soil and ground water system in which is entered from the soil leaching processes, so that it comes to the eutrophication of stagnant water (lakes), which become swamp.
Concentration in the air
According to the data of the (WHO) global annual average urban concentrations of NO2 range between 20 and 90 μg/m3.
Long term monitoring of NO2 in the air on a European stations shows a decrease of average annual concentrations by 12% in the period from 1997. to 2001.
European Union IPA 2013 Programme for Croatia

## Slide 55: 2.3 NO2 – SPATIAL AND TEMPORAL DISTRIBUTION
Average annual concentrations of NO2 in Europe on the measuring stations AirBasea during the period from 1997. to 2001.
Source: AIRNET.
Average annual concentrations of NO2 categorized according to the location of the measurement.
Source: AIRNET.
European Union IPA 2013 Programme for Croatia

## Slide 56: 2.3 NO2 – SPATIAL AND TEMPORAL DISTRIBUTION
Average annual concentrations of NO2 categorized according to a source of pollution. Source: AIRNET.
Background
Industrial
Traffic
European Union IPA 2013 Programme for Croatia

## Slide 57: 2.3 NO2 – SPATIAL AND TEMPORAL DISTRIBUTION
Average annual concentrations of NO2 in the world in the period of 2002. to 2005. Source: Air quality guidelines – the WHO.
European Union IPA 2013 Programme for Croatia

## Slide 58: 2.4 NO2 – TOXICOLOGICAL AND PUBLIC HEALTH ASPECTS
The path of entering NO2 into the organism is a respiratory system.
It's very reactive, but poorly soluble in water, so its biological effects result primarily from his reaction with lipids and protein.
After inhalation 70 to 90% of gas is absorbed into the respiratory system. People who are physically active absorb an even higher percentage of NO2 and it is transmitted to the lower parts of the respiratory system up to the pulmonary alveoli.
European Union IPA 2013 Programme for Croatia

## Slide 59: 2.4 NO2 – TOXICOLOGICAL AND PUBLIC HEALTH ASPECTS
After entering the respiratory system NO2 rapidly enters the bloodstream. Primary products found in the bloodstream are NO2- and NO3- ions that were created by dissociation of nitrogen and nitric acid formed in the NO2 reaction with water in the tissues. Since NO2 gas having an unpaired electron, giving it a free radical, is highly reactive and capable of oxidizing cellular molecules.
This property results in the creation of:
inflammatory processes in the tissues
cellular damage
lipids peroksidation
interaction with cellular proteins and thiols..
All of that damage lung tissue.
European Union IPA 2013 Programme for Croatia

## Slide 60: 2.4 NO2 – TOXICOLOGICAL AND PUBLIC HEALTH ASPECTS
The ambient concentration of NO2 do not cause negative health effects
The increased concentration in the range of 300 to 3000 μg/m3 that we find in the tunnels at the short-lived exposure can cause inflammatory reactions in the lung tissue, as well as a reduction in lung function
In patients with asthma and COPD, concentration of 190 μg/m3 can cause significantly narrowing of the airways
European Union IPA 2013 Programme for Croatia

## Slide 61: 2.4 NO2 – TOXICOLOGICAL AND PUBLIC HEALTH ASPECTS
In patients with a mild form of asthma, 30-minute exposure to concentrations of 380 up to 560 μg/m3 may cause reversible decrease in lung function.
(The WHO Air quality guidelines, AIRNET).
European Union IPA 2013 Programme for Croatia

## Slide 62: 2.4 NO2 – TOXICOLOGICAL AND PUBLIC HEALTH ASPECTS
Recommended values (μg/m3), for concentration of nitrogen dioxide (NO2) in the air-the WHO
Pollutant
Averaging time
Temporary goal 1
Temporary goal 2
Temporary goal 3
Recommended value
hour
year
European Union IPA 2013 Programme for Croatia

## Slide 63: 2.5 NO2 – MEASUREMENT METHODS
The reference method for the measurement of the NO and NO2
Prescribed by regulations of the Republic of Croatia and the European Union. In the European Union and Croatia was adopted by 2012.
chemiluminescence
(HRN EN 14211)
European Union IPA 2013 Programme for Croatia

## Slide 64: 2.5 NO2 – MEASUREMENT METHODS
The fundamental principle of chemiluminescence is the emission of energy (radiation) that is the result of some chemical reaction that occurs in this case due to the reaction of nitrogen oxide with ozone:
NO + O3  NO2* + O2
NO2*  NO2 + hv
[1]
[2]
In reaction [1] nitric oxide is generated in the excited energy state (NO2 *) which is then returned to normal state [2] by release of energy whose intensity is proportional to the concentration of NO from the reaction [1].
European Union IPA 2013 Programme for Croatia

## Slide 65: 2.5 NO2 – MEASUREMENT METHODS
The energy emitted by this reaction is in the near infrared part of the spectrum (600-3000 nm) with a strong intensity of about 1200 nm. The emitted energy is filtered using selective optical filters and then converted to an electric signal with the aid of a photoconductor or photodiode. The electrical signal is then measured and its intensity is proportional to the NO concentration that has entered the reaction [1].
In the chemiluminescent analyzer, the air flows through the reaction cell at constant speed with optimized conditions and the presence of excess ozone. This ensures complete reaction.
European Union IPA 2013 Programme for Croatia

## Slide 66: 2.5 NO2 – MEASUREMENT METHODS
In the process of determining the concentration of nitrogen dioxide (NO2) the air is first passed through a catalytic converter where all NO2 converts to NO:
NO2 --------catalytic conversion--------NO
[3]
Thus, NO represents the sum of NO from the air and the NO generated by the conversion from NO2 and we call it NOX. NO passes through the reaction cell and the concentration is determined as described above. By the alternating passage of sampled air through the passing cell and without passing through the converter, the concentrations of NO and NOX (NO + NO2) in the air are obtained. The difference between these concentrations is the concentration of NO2 in the air:
European Union IPA 2013 Programme for Croatia

## Slide 67: 2.5 NO2 – MEASUREMENT METHODS
NOx – NO = NO2
[4]
If the instrument is calibrated in volume / volume units, NO and NO2 concentrations are directly measured in volume / volume units (ppb) since the chemiluminescence intensity is proportional to the NO concentration in volume / volume units.
After that, the obtained concentrations in ppb are converted to μg/m3 using the standard conversion factors for a temperature of 20 ° C and an atmospheric pressure of 1013 hPa.
1ppb (nmol/mol) NO = 1,25 μg/m3 NO
European Union IPA 2013 Programme for Croatia

## Slide 68
THANK YOU FOR YOUR ATTENTION !
  Disclaimer: The contents of this publication are the sole responsibility of EKONERG – Energy Research and Environmental Protection Institute, Ltd. and can in no way be taken to reflect the views of the European Union
This project is funded by the European Union